## Slide 1: CISCO VIRTUAL INTERNSHIP ACTIVITY Design of secure College campus network. KLE TECHNOLOGICAL UNIVERSITY
NAME: A.SANIYA
USN: 01FE18BEC351
School Of Electronics & Communication

## Slide 2: 3D of Cyber Security
Technology
Policies & Practices
People

## Slide 3: OVERVIEW:
1.Types Of Attacks and Solutions.
  End Device Attacks.
  Vulnerabilities.
  Management Protocols.
  2. Secure Network for Institution.
  3.Topology
  Lab 1.
  Classroom
  Staffroom

## Slide 4: Types Of Attacks & Solutions :

## Slide 5: 1.END DEVICE ATTACKS
Laptops, Desktops, servers and IP phones as well as employee-owned devices comes under End devices.
ATTACKS:
  Endpoints are particularly susceptible to malware related attacks that originate through email or web browsing. Eg: Viruses, worms & Trojen Horses.
  They are also susceptible to attacks such as Spyware, Adware, Botnet & Zombies which can damage the host system and can also capture the host data.
SOLUTION:
  Endpoints have typically used traditional host-based security features, such as antivirus/anti-malware, host-based firewalls, and host-based intrusion prevention systems(HIPSs).
  End devices can be protected by a combination of NAC, AMP(Advanced Malware Protection)software, an email security appliance(ESA), and a web security appliance(WSA)

## Slide 6: 2.VULNERABILITIES
Vulnerabilities comes under Layer 2 attack of OSI reference model i.e., Data link layer. If a threat actor gets access to Layer 2 then he may damage the above layers also irrespective of how much security has provided to it.
ATTACKS:
CATEGORY | EXAMPLES
MAC Table Attacks | Includes MAC Address Flooding Attacks
VLAN Attacks | Includes VLAN hopping and VLAN doubling attacks. It also includes attacks between devices on a common VLAN.
DHCP Attacks | Includes DHCP Strarvation and DHCP spoofing attacks.
ARP Attacks | Includes ARP spoofing and poisoning attacks.
Address Spoofing Attacks | Includes MAC address and IP address spoofing attacks.
STP Attacks | Includes spanning Tree Protocol manipulation attacks

## Slide 7: .
SOLUTION:
SECURING MANAGEMENT PROTOCOLS:
Using management protocols such as SSH, Secure Copy Protocol(SCP), Secure FTP(SFTP), and Secure Socket Layer/Transport Layer Security(SSL/TLS).
Using a dedicated management VLAN where nothing but management traffic resides.
Solution | Description
Port Security | Prevents many types of attacks including MAC address flooding attacks and DHCP starvation attacks.
DHCP Snooping | Prevents DHCP Starvation and DHCP spoofing attacks
Dynamic ARP Inspection(DAI) | Prevents ARP spoofing and ARP poisoning attacks.
IP Source Guard(IPSG) | Prevents MAC and IP address spoofing attacks.

## Slide 8: Secure Network for Institution
Devices protected by FireWalls.
Disabling all unused ports in switches.
Setting VLAN’s for different Users to prevent from Vulnerabilities.
Setting SSH for configuring routers/switches from remote host with secured password and also to secure management protocols.
Setting WEP password for wireless network connections.
Used Web Cameras for more security.

## Slide 9: Topology:
I have created 3 areas
Lab-1:
SERVER | ROUTER | SWITCH | PC/End Devices
Server protected by Firewall | Used SSH Protocol to configure from end devices. Rsa : ece.office Username :faculty Password : student | Created 2 VLAN’s for Students and administrator’s respectively. Disabled fa 0/12-24 to be more secure on switch 1. Similarly for switch 2 fa 0/8-24 are down. | Total of 24 PC’s have been used for LAB-1 divided into Student and admin VLAN respectively. 1 printer is also set up.

## Slide 10: 2.Classroom
Classroom needs wireless connection .
WIRELESS ROUTER | SWITCH | END DEVICES
Encrypted with strong password(WEP) to avoid being used by strangers and hackers. Password:cisco | Switch numbers from fa 0/6-25 are down to be secure. Also can be configured from end devices using SSH protocol. Username and password are same as Lab-1. | 3 PC’s are connected through ethernet cables. 2 PC’s are connected wirelessly. A Laptop, Smartphone , Tablet and cameras are also connected wirelessly .

## Slide 11: 3.Staff Room
SERVERS | ROUTERS | SWITCH | END DEVICES
All servers protected by Firewalls. | SSH protocol to be easily configurable from end devices. | 2 VLAN’s for faculty and admins respectively. Disabled all unused ports. | PC’s and printers. PC’s virtually protected by FireWalls.

## Slide 12: THANK YOU